Electronics left on for 5 minutes to heat up.

(note that all radioactive materials are old and have hence reduced by a number of half-lives)

Calibration material:
-Caesium-137, 662 keV
-Americium-241, 59.5 keV

Angles were measured by taking the left and right side of the detector and finding the average.
The uncertainty on this was determined to be 0.25 degrees based on half the resolution of the graduation.

Note to self, don’t accidentally clear the graph

Measurements taken from the minimum to the left of the peak and to the end of the tail to the right of the peak. Note that to calculate the net counts the software assumes a linear transition between the minimum to the left and the tail to the right due to multiple scattering.

Measurements taken up to at least a net counts of 10k

Note counts were stopped near 20 degrees off axis due to the likely introduction of direct detection from the source.